## Slide 1: Planning Satellite Swarm Measurements for Earth Science Models: Comparing Constraint Processing and MILP Methods Rich Levinson1,2 Samantha Neimoeller1 Sreeja Nag1,3 Vinay Ravindra1,3 {rich.levinson, samantha.c.niemoeller, sreeja.nag, vinay.ravindra} @nasa.gov 1NASA Ames Research Center 2 KBR Wyle Services, LLC 3 Bay Area Environmental Research Institute Moffett Field, CA 94035 Collaborators: Mahta Moghaddam (University of Southern California) Daniel Selva (Texas A&M University) Funded by: NASA Earth Sciences Technology Office (ESTO)

## Slide 2
Soil Moisture Prediction
Soil moisture is a key indicator for predicting floods, mudslides, wildfires, other phenomena
Problem:
We have initial solution for improving soil moisture prediction
Our Constraint Processing planner follows a narrow beam of heuristically guided trajectories through a huge search space
We don't know how optimal our heuristic solution is
Research Questions:
How close to optimal is our heuristic solution?
Can we model our constraints in Mixed Integer Linear Programming (MILP)?
How long would it take MILP to prove optimality on our 6-hour plan horizon?
(NOAA/National Weather Service website)
Background and Motivation
Notes: Dynamic Constraint Processing means the set of decision variables changes during the solving process. In our case decision variables are removed when we propagate choices forward in time, so the solution node has fewer decision variables than the root.

## Slide 3
Dynamic Constraint Processing vs. Mixed Integer Linear Programming
Flexible Constraints & Search Control
Speed & Scalability
DCP
MILP
Dynamic Constraint Programming (DCP)
  Suboptimal but Fast
  Constraints enforced "on-demand"
  Variables dynamically eliminated by constraint handlers
Mixed Integer Linear Programming (MILP)
  Optimal but Slow
  Less flexible constraint modeling
  Quantitative declarative constraints
  Scalability challenges

## Slide 4
D-SHIELD: Distributed Spacecraft w/ Heuristic Intelligence to Enable Logistical Decisions
Multiple satellites w/ multiple instruments to observe Ground Positions (GP)
Each satellite has 2 different sensors & can point at 61 different angles
Each observation covers multiple GP (9 km x 9 km tile)
For each satellite: Assign a sensor command for every Time Point (TP) when it can see any GP
GP#2
GP#1
GP#3

## Slide 5
D-SHIELD Constraints
Constellation-wide constraint
Duplicate Observations: No duplicate GP observations (across all satellites)
Satellite-level mutex constraints (only do one thing at a time)
Image Lock – hold viewing angle for 3 seconds per observation
Maneuver constraints – slew time for changing view angle

## Slide 6
Search space for each satellite:
Access times (TP)
Command choices (sensor & view angle) for each access time (TP)
List of GP covered by each command
Planner Input: GP Access Times & Command Choices
Timepoint (TP) | Command Choices | Ground Positions (GP) covered by command
10 | L.32 (L-band, angle 32) | 25, 26, 27
 | P.32 (P-band, angle 32) | 24, 25, 26, 27, 28
 | P.34 (P-band, angle 34) | 36, 38, 40, 47, 49

## Slide 7
Planner Input: Prediction and Measurement Errors
Ground Position (GP) | Timepoint (TP) | Prediction Error
15 | 100 | 0.02
 | 500 | 0.23
Sensor Command | Ground Cover | Measurement Error
L.48 |  | 
 | Forest | 0.035
 | Shrubs | 0.025
Measurement Error
Soil Moisture Prediction Error
Error increases with time and rain
Error decreases with "good" observation (measurement error < pred. error)

## Slide 8
Planner Input: Prediction and Measurement Errors
Ground Position (GP) | Timepoint (TP) | Prediction Error
15 | 100 | 0.02
 | 500 | 0.23
Sensor Command | Ground Cover | Measurement Error
L.48 |  | 
 | Forest | 0.035
 | Shrubs | 0.025
Measurement Error
Soil Moisture Prediction Error
Goal: Observe GP having most prediction error,
using measurements with least error

## Slide 9
Scenario: 3 satellites, 6-hour plan horizon:
~8700 Time Points (TP) when GP are visible
~55 command choices/TP (max: ~150 choices/TP)
# nodes in search space
Search Space Combinatorics
1.7m GP total
(global)
765k GP visible in 6 hrs
17k fit in 6 hr plan
= 558700 = "Infinity"

## Slide 10
Dynamic Constraint Processing (Levinson et al., IWPSS '21)
Qualitative Decision Variables:
= the command choice for sat s at time t. {All TP when sat s can see any GP}
{L.32, L.34, P.33, P.34}
Constraints are procedural (Python code) and called on-demand after each planner choice
MILP: Binary Decision Variables
= 1
= 1
Constraints are quantitative, declarative, and pre-enumerated
Apples-to-Apples comparison:
Requires identical inputs, model constraints, and metrics
Different Planning Models

## Slide 11
Objective: Maximize reduction of GP model error
maximize
commandReward (s, c, t) = reward for sat s executing cmd c at time t
=
TP | Cmd | Observed GP | Command Reward
10 | L.32 | 25, 26, 27 | 0.25
20 | P.21 | 33,35,39,40 | 0.32
30 | p.25 | 50,21 | 0.20
objective: cmd rewards |  |  | 0.77
gpReward(g,c,t) = reward for viewing with command c at time t
= where = prediction error for at time t
= measurement error for command c in biome
Plan:

## Slide 12
Comparison: Science Value
Chart: Objective (total error reduction) =
| Case 1 | Case 2 | Case 3 | Case 4 | Case 5
DCP | 15.8 | 9.7 | 22.9 | 99.6 | 101.2
MILP (optimal) | 23.7 | 17.2 | 38.7 | 171.6 | 174.7
Chart: # of GP observed
| Case 1 | Case 2 | Case 3 | Case 4 | Case 5
DCP | 948 | 666 | 1181 | 3113 | 3140
MILP (optimal) | 1032 | 620 | 1212 | 4010 | 4200
6 test cases with increasing plan horizons and complexity
Cases 1 – 5: DCP achieves ~ 60 % optimal
Case 6: Unsolvable by MILP in 50 hour time limit, but DCP solves in 28 mins

## Slide 13
Comparison: Efficiency
Chart: Error reduction/command
| Case 1 | Case 2 | Case 3 | Case 4 | Case 5
DCP | 0.035189 | 0.038189 | 0.060743 | 0.060145 | 0.061858
MILP (optimal) | 0.058809 | 0.088205 | 0.13119 | 0.11689 | 0.1186
Chart: Error reduction/GP
| Case 1 | Case 2 | Case 3 | Case 4 | Case 5
DCP | 0.016667 | 0.014565 | 0.01939 | 0.031995 | 0.032229
MILP (optimal) | 0.022965 | 0.027742 | 0.031931 | 0.042793 | 0.041595
MILP is always more efficient with higher objective rewards per command and per GP
MILP plans always has fewer commands (makespan): Less slewing & energy cost

## Slide 14
Comparison: Model Size
Chart: # Decision Variables (MILP is log scale on right)
| Case 1 | Case 2 | Case 3 | Case 4 | Case 5 | Case 6
DCP | 1705 | 900 | 1468 | 7464 | 7527 | 8701
MILP | 26959 | 89118 | 122675 | 244207 | 244363 | 1856154
Chart: # Constraints (MILP only, log scale)
| Case 1 | Case 2 | Case 3 | Case 4 | Case 5 | Case 6
MILP | 914000 | 14400000 | 16800000 | 20800000 | 20000000 | 90000000
DCP: Scales linearly with # of timepoints
# variables = # Timepoints in plan horizon
# constraints is N/A because they are instantiated on demand
MILP: Always requires many more variables and constraints
# vars =
∝ (mutex deconfliction)

## Slide 15
Conclusion
 | DCP | MILP
Optimal |  | 
Plan Efficiency |  | 
Speed |  | 
Flexible Constraints |  | 
Heuristic Search Control |  | 
Model Size/ Scalability |  | 
Both methods are useful, especially when used together

## Slide 16
Future Work
Search Control:
  Monte Carlo Tree Search (MCTS)
  Divide & Conquer (independent subproblems with TP gap delimiters)
Closing the execution loop
  Simulated satellites execute their plans with noise
New constraints:
  Relaxed 3-second image lock (not yet modelled in MILP)
New domain:
  wildfire prediction

## Slide 17
Questions?
rich.levinson@nasa.gov
video
Thank You

## Slide 18
Experiments
Experiments ran on: 2020 MacBook Pro 13-inch 2.3 GHz Quad-Core Intel Core i7, 32 GB RAM.
DCP solutions implemented in Python
All MILP solutions used Gurobi 9.5.
Data sets and software will be released open source

## Slide 19
Experiment includes 6 test cases varying by:
Plan horizon
  1,000 secs (~17 mins)
  1,800 secs (30 mins)
  7,200 secs (2 hours)
  21,600 secs (6 hours)
Rainy or non-rainy GP cohort (rainy GP recently received rain)
Triage heuristic
  solve for the 15% most needy GP first
  mitigation for MILP model size combinatoric explosion
Six Test Cases

## Slide 20
Planner Objective: Maximize model improvement (error reduction)
Each GP: prior model error & cmd choices w/ measurement errors
Error(GP) = F(time, rain, biome type, instrument(s), view angle)
Error increases with time and rain
Error decreases with "good" observation (measurement error < model error)
GP | TP | Model Error | cmd | Measurement Error
2 | 27 | 0.08 | L.41 | 0.14
 | 1500 | 0.39 | P.48 | 0.07
GP | Model Error | cmd | Measurement Error
2 | 0.39 0.07 | P.48 | 0.07

## Slide 21
For each satellite: Search space of access times, viewing options (commands), and covered GP
Command choice examples: L.34 = <L-band, angle 34> ,
P.32 = <P-band, angle 32> TP Command
(time) choices GP covered by choice
1311: L.32: [3165]
L.34: [3445, 3446]
P.33: [3165]
L.32 & P.32: [3165]
Planner Input: GP Access Times and Command Choices

## Slide 22
observation results (image data)
Planner output: Satellite command sequences (per sat)
Planner inputs: GP view times, command choices, soil moisture model errors, measurement errors
GP model errors
Planner
Objective: reduce GP model error
Satellite 2 (simulated) command execution
Soil Moisture Predictor
Preprocessing
Prepare raw science data for planner
Science Inputs:
Ground Positions (GP)
w/ biome type (shrub, forest, baren)
GP access times w/ viewing cmd options
Measurement error model
Slew time & energy requirements
Observed & predicted rain
Ground sensors
Spacecraft & instrument h/w specs
D-SHIELD Architecture
GP | TP | Model Error
1 | 100 | 0.03
 | 500 | 0.23
2 | 200 | 0.20
 | 700 | 0.26
Satellite 1 (simulated) command execution
Sensor | Angle | Measurement Error
L-Band | 48 | 0.035
P-Band | 50 | 0.021
L-Band & P-Band | 42 | 0.025
Measurement errors

## Slide 23
Search Space Combinatorics
TP 1
55
55
55
Tree depth:
8700
Each node is a decision var associated with a TP
~55 children/node (~55 cmd choices/TP)
Tree Depth: 8700 = # of TP
TP
8700

## Slide 24
2 Binary Decision Variables
= 1 ,
= 1
Duplicate GP constraint:
Mutex constraint (image lock and slew times block out other commands)
GP Coverage Constraint: Tracks which GP are covered by planned commands
Objective: maximize the sum of gpRewards for all GP covered by plan:
Planner Model (MILP)

## Slide 25
DCP vs. MILP: Model Size and Performance
MILP could not solve 6-hour plan horizon within 50 hours, but DCP solves it in 28 minutes.
MILP requires many more vars and constraints
MILP makespan is always smaller

## Slide 26
gpReward(g,c,t) = reward for viewing with command c at time t
= =
where = prediction err for at time t
= measurement error for command c in biome type
cmdReward(s,c,t) = sum of gpRewards for all GP observed by sat s using cmd c at time t
=
where = set of GP visible by sat s using cmd c at time t
Objective: Maximize (3)
max sum of all gpRewards for all GP covered by all commands in plan P
Identical metrics for DCP/MILP comparison: Equations 1, 2 and 3
Objective: Maximize reduction of GP model error

## Slide 27
Conclusion
Dynamic Constraint Processing (DCP) | Mixed Integer Linear Programming (MILP)
Pro Speed Better search control Flexible modeling Domain heuristics Explainable AI | Pro Provably optimal solutions Relies on 3rd party solver (benefit of robust, heavily tested tool)
Con Suboptimal solutions Subject to local minima and path dependencies | Con Slow Limited model flexibility Difficult to include domain specific heuristics Solver variability Declarative model requires pre-enumerating 10's of millions of constraints in model Variable domains, constraints must be quantitative

## Slide 28
Satellite 2 Timepoint (TP) choices:
Command choices and times for viewing each GP (per satellite)
Command search space, 1 file for each satellite
Command choice examples: L.32 = <L-band, angle 32> ,
P.34 = <P-band, angle 34> Cmd
Time choices GP covered by choice
1311: L.32: [3165]
L.34: [3445, 3446]
P.33: [3165]
P.34: [3445, 3446]
P.35: [3445, 3446]
L.32 & P.32: [3165]
Planner Input and Output
Satellite 1 Timepoint (TP) choices: Command choices for each TP
Command search space = choices for every TP when a sat can observe GP
1 file for each satellite
Command choice examples: L.34 = <L-band, angle 34> ,
P.32 = <P-band, angle 32> TP Command
(time) choices GP covered by choice
1311: L.32: [3165]
L.34: [3445, 3446]
P.33: [3165]
L.32 & P.32: [3165]
Ground Position (GP) choices:
Choices for when & how to view each GP
Science-value search space
Measurement error depends on GP biome-type (shrub, forest, baren)
One file for whole constellation
Choices for GP: 3165
TP Cmd Pred. Meas.
Sat (time) Choices Error Error
1 1311 L.32 .008 .038
1 1311 P.33 .008 .017
1 1311 L.32 & P.32 .008 .010
2 1259 L.33 .042 .028
2 1259 P.33 .042 .028
Satellite 2 Plan:
Time Command
[2-4] P.48
[5-14] Idle
[15-17] L.48
[18-36] Idle
[37-40] Slew
[41-43] L.44
Satellite 1 Plan:
Time Command
[2-4] P.48
[5-14] Idle
[15-17] L.48
[18-36] Idle
[37-40] Slew
[41-43] L.44
Inputs: TP and GP choices
Outputs: Plans for each satellite

## Slide 29
All constraints are enforced via choice propagation (forward consistency checking)
Implemented by propagateChoices(variable, value)
Duplicate observation constraint handler examples:
  Example 1: After observing GP 123, remove it from all future var domains (for all sats)
  [: {L.32: [123],
  L.33: [436349, 436350, 436351]]
  Example 2: Removing GP results in empty variable domain, so remove the variable
  [: {P.42: [253]}]
Empty variable domain means no observation can be taken at that time (unlike pure CSP)
Image Lock and Slew time constraints remove variables for infeasible observation times
Constraint Handlers